## Slide 1
Advisors: Prof. Dr. André Seyfarth, Prof. Dr. Klaus Gramann, Dr. Maziar A. Sharbafi
Motivation and Research Challenge
The problem
Exoskeletons are usually tuned to save energy or muscle activity [1]
But people decide whether to keep a device by how it feels
Which factors do people actually weigh when they judge assistance? We do not know.
Why it matters
A device that saves energy but feels wrong will be rejected
Knowing the user’s own criteria allows assistance that people accept and want to use [2]
My Approach
Two studies: what makes a device feel right?
Study 1 · done: knee exoskeleton, seated
From a controlled single joint movement to natural walking
Study 2 · starting now: hip exoskeleton, walking
High resist
Low resist
Zero torque
Low assist
High assist
Very high assist
Current Status
Study 1: knee exoskeleton · paper ready [3]
A unique regional fingerprint of the physical demand imposed by the exoskeleton on the cortical dynamics
Which brain signals carry the judgement, not only the demand?
How Could Others Help Me? How Could Others Benefit From my Research?
I am looking for…
I can offer…
[1] Sawicki et al. (2020) J NeuroEng Rehabil 17:25. [2] Ingraham, Remy & Rouse (2022) Sci Robot 7:eabj3487. [3] Khosrotabar, Gramann, Seyfarth, Vogt & Sharbafi. Sensorimotor cortex reflects human-exoskeleton interaction level (manuscript). [4] Bakdash & Marusich (2017) Front Psychol 8:456.
Dual functionality: the exoskeleton assists, and its six modes probe how brain and body respond
Dual evaluation: expert measures (EEG, muscles, energy, gait kinematics) linked to each user’s own judgement
Behaviour: Perceived difficulty increased from 1.8 to 7.0 unit
Which terms matter, and how much, for each person?
Energy
Muscle Effort
Stability
Naturalness
Predictability
Control
Judgement = Σ wi · termi
wi = ?
THE HUMAN COST FUNCTION
Scan for the Questionnaire
What remains unclear
14 participants
A visuo-motor tracking task while the exoskeleton applies 3 levels of physical demand
EEG, knee flexors and extensors, and subjective evaluations were recorded
Flexion
Extension
Air compressor & Pressure valve
Low demand (P = 1 bar)
Medium demand (P = 3 bar)
High demand (P = 6 bar)
Pressurised
PAM shape
Medium
High
6 bar
Reference Tracking
Knee Angle
Ref. Trajectory
Horizontally moving reference path
Extension
Flexion
Brain: 64-channel mobile EEG
Body: EMG, Kinematics (IMU), GRF, energy cost
Experience: Custom-designed questionnaire
24 participants, 2 days each, 6 modes:
Link to the LokoAssist core ideas
Psychology and human factors: validating short rating scales; agency, embodiment and trust
An open dataset: brain, body and experience, different interaction levels
An open questionnaire for your own device study
Our mobile brain/body lab: add EEG and muscle recordings to your study
Neuromechanics of Human-Exoskeleton Interaction:
Brain, Body and Experience
Morteza Khosrotabar, Project Area B2, Lauflabor Locomotion Laboratory, TU Darmstadt
Right sensorimotor cortex (n = 12): Alpha & beta power decrease step by step with demand
Left parieto-occipital cortex (n = 13): Task-locked modulation in theta & alpha power, independent of the demand
Muscles 26%
Not explained by muscles or tracking error: 73%
Study 2: hip exoskeleton (pilot, n = 4)
What goes with a pleasant walk? How walking felt, not energy
Compared with zero torque, resisting modes raised energy cost by about 10 to 25%; high assistance saved about 5 %
The strongest assistance did not feel like help (3 of 4 rated it as hindering)
Repeated-measures correlation [4]; descriptive only